## Slide 1: Network Security Monitoring at 100Gbps
Kashif Mohammad
University of Oxford
Information Security Operations Team(OxCERT)
Notes: Good afternoon Everyone, My name is Kashif Mohammad and I am head of Information Security operations Team at the University of Oxford. This is the first time, I am attending a Trusted Introducer Event so I will take this opportunity to give a brief overview of University of Oxford InfoSec Team and why Oxford University is a unique institution in term of managing cyber security
Then I will go topic of this presentation is Network Security Monitoring at 100Gbps.

## Slide 4: Information Security Team
50K Users
150K Devices
320 Email Domains
38 Colleges
110 Departments and Centers
CISO
OxCERT(8)
GRC(6)
Infosec Team
120 SubEstates

## Slide 5: Network Monitoring at 100Gbps
Requirements
Detection of malicious activities on the network
Pattern of abusive behavior over time
Regulatory requirements
Passive Monitoring
Challenges
Cost
Scalability
Resilience
Integration with the existing tools
Data ingest and storage
Extreme optimization

## Slide 6: Market Research

## Slide 7: Setup Design
Net Flow
100Gbps Tx
Internet
University Backbone
100Gbps Rx
TAP
Packet Broker
IDS
200Gbps full duplex LAG
200Gbps
FPGA Card
25Gbps
NIC
200Gbps full duplex LAG

## Slide 8
Napatech NT200A02 FPGA Card
/opt/napatech3/bin/ntpl -e "Delete = All"
/opt/napatech3/bin/ntpl -e "HashMode = Hash2TupleSorted"
/opt/napatech3/bin/ntpl -e "Assign[StreamId=(0..15)] = All"
Traffic Capture for Netflow Genaration

## Slide 9
FPGA Card
PF_RING ZC
Cento
Kafka Topic
Special thanks to Ntop for providing free academic licenses for PF_RING ZC and Cento
Netflow Generation

## Slide 10
Using 22000 out of 60000 (Aprox) rules provided by the ETpro
enabled_group:
malware:
- trojan-activity
- successful-user
- successful-admin
- command-and-control
- attempted-admin
exploit:
- successful-admin
- command-and-control
- web-application-attack
- web-application-activity
- suspicious-login
- attempted-admin
trojan:
- trojan-activity
- successful-admin
worm:
- trojan-activity
current_events:
- trojan-activity
hunting:
- misc-activity
enabled_sid:
- '2027472'
- '2046188’
- ……
disabled_sid:
- '2029992'
Intrusion Detection System

## Slide 11
Packet Steering
NUMA Node and CPU affinity
Receive Side Scaling(RSS)
Intel XV710 25 Gb NIC
25Gbps Full duplex
System Performance Optimization

## Slide 12
usr/bin/ip link set enp59s0f1 promisc on arp off up
usr/bin/ip link set enp59s0f1 mtu 9000
usr/sbin/ethtool -L enp59s0f1 combined 32
usr/sbin/ethtool -K enp59s0f1 rx off
usr/sbin/ethtool -K enp59s0f1 tx off
usr/sbin/ethtool -K enp59s0f1 tso off
usr/sbin/ethtool -K enp59s0f1 gso off
usr/sbin/ethtool -K enp59s0f1 gro off
usr/sbin/ethtool -K enp59s0f1 rxhash on
usr/sbin/ethtool -K enp59s0f1 ntuple on
usr/sbin/ethtool -K enp59s0f1 sg off
usr/sbin/ethtool -K enp59s0f1 txvlan off
usr/sbin/ethtool -K enp59s0f1 rxvlan off
usr/sbin/ethtool -X enp59s0f1 hkey 6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A:6D:5A equal 32
usr/sbin/ethtool -N enp59s0f1 rx-flow-hash tcp4 sd
usr/sbin/ethtool -N enp59s0f1 rx-flow-hash tcp6 sd
usr/sbin/ethtool -N enp59s0f1 rx-flow-hash udp4 sd
usr/sbin/ethtool -N enp59s0f1 rx-flow-hash udp6 sd
usr/local/bin/set_irq_affinity 2,4,6,8,10,12,14,16,18,20,22,24,26,28,30,34,36,38,40,42,44,46,48,50,52,54,56,58,60,62 enp59s0f1
Most of these optimizations are based on Peter Manav’s Suricata Extreme Performance guide https://github.com/pevma/SEPTun-Mark-II
NIC Optimization

## Slide 13
K
I Kibana
Elasticsearch
Logstash
Processing Nodes
(2 locations)
Master Nodes
(3 locations)
Data Nodes Hot
(2 locations)
Load Balancer
(1 locations)
Kibana Nodes
(2 locations)
Logstash
Forwarder Nodes
(2 locations)
Queue Servers
(2 locations)
IDS Alerts
NTOP Cento
Visualization & Analysis
Indexing & storing
Processing & Enrichment
Queue
Forwarder & Triage
Data Collection
ElasticSearch

## Slide 14
4 Billion events/day
800GB of data/day

## Slide 15
IDS Dashboard

## Slide 16: Thank You
Questions?